## Slide 1: Practice 3 Operational Amplifiers
Nikolay Nikolaev (nanikolaev@itmo.ru)
Nikolai Poliakov (polyakov_n_a@itmo.ru)
Roman Olekhnovich (r.o.olekhnovich@mail.ru)
Notes: Hello. We are starting our Practice 3 «Operational amplifiers. Wien Bridge Oscillator »
The course focuses "Место для уравнения."on the analog and digital components of electronic circuits which can be used in control systems area.

## Slide 2: Summary
Wien Bridge Oscillator
Practice work 2: simulation
Control test

## Slide 3: Wien Bridge Oscillator
If, in particular, the values are R1 = R2 = R and C1 = C2 = C,
the resulting oscillator frequency is
Notes: A practical oscillator circuit uses an op-amp and RC bridge circuit, with the oscillator frequency set by the R and C components. Figures on slide shows a basic version of a Wien bridge oscillator circuit.
The Wien Bridge Oscillator is so called because the circuit is based on a frequency-selective form of the Wheatstone bridge circuit. The Wien Bridge oscillator is a two-stage RC coupled amplifier circuit that has good stability at its resonant frequency, low distortion and is very easy to tune making it a popular circuit as an audio frequency oscillator
Note the basic bridge connection resistors R 1 and R 2 and capacitors C 1 and C 2 form the frequency-adjustment elements, and resistors 3 and 4 form part of the feedback path. The op-amp output is connected as the bridge input at points a and c. The bridge circuit output at points b and d is the input to the op-amp.
Neglecting loading effects of the op-amp input and output impedances, the analysis of the bridge circuit results in
Thus a ratio of R 3 to R 4 greater than 2 will provide sufficient loop gain for the circuit to oscillate at the frequency calculated using Eq .

## Slide 4: Wien Bridge Oscillator
If, in particular, the values are R1 = R2 = R and C1 = C2 = C,
the resulting oscillator frequency is
Notes: A practical oscillator circuit uses an op-amp and RC bridge circuit, with the oscillator frequency set by the R and C components. Figures on slide shows a basic version of a Wien bridge oscillator circuit.
The Wien Bridge Oscillator is so called because the circuit is based on a frequency-selective form of the Wheatstone bridge circuit. The Wien Bridge oscillator is a two-stage RC coupled amplifier circuit that has good stability at its resonant frequency, low distortion and is very easy to tune making it a popular circuit as an audio frequency oscillator
Note the basic bridge connection resistors R 1 and R 2 and capacitors C 1 and C 2 form the frequency-adjustment elements, and resistors 3 and 4 form part of the feedback path. The op-amp output is connected as the bridge input at points a and c. The bridge circuit output at points b and d is the input to the op-amp.
Neglecting loading effects of the op-amp input and output impedances, the analysis of the bridge circuit results in
Thus a ratio of R 3 to R 4 greater than 2 will provide sufficient loop gain for the circuit to oscillate at the frequency calculated using Eq .

## Slide 5: Wien Bridge Oscillator
Choose real capacitor
=

## Slide 6: Wien Bridge Oscillator

## Slide 7: Wien Bridge Oscillator

## Slide 8: Wien Bridge Oscillator

## Slide 9: Wien Bridge Oscillator

## Slide 10: Wien Bridge Oscillator

## Slide 11: Wien Bridge Oscillator

## Slide 12: Wien Bridge Oscillator
10.44kHz
11.11kHz
= =11,129kHz
Real operational amplifier
Ideal operational amplifier

## Slide 13: Wien Bridge Oscillator
Real operational amplifier
Ideal operational amplifier

## Slide 14: Test 2
https://forms.yandex.com/cloud/6372342c5d2a0664e323da80/
https://clck.ru/32gh38
1st deadline: 15.11.2022 15:15 (GMT +8)

## Slide 15: Practice 3
1st deadline: 25.11.2022 15:15 (GMT +8)

## Slide 16: Thanks for your attention!